## Slide 1: Project Update
Yannik Zobus, Udo Eisenbarth
THRILL WP 3.4
“Supporting calculations for system design”

## Slide 2: THRILL WP 3.4 - “Supporting calculations for system design”
Modern high-intensity laser systems become more sophisticated & complex
Rigorous planning is crucial to make systems sustainable
Full-scale modeling of these systems, ideally creating a “digital twin” is necessary!
However, existing modeling solutions are
Proprietary:
  hard / impossible to integrate, expensive
Self-written codes:
  Often „single-use“ during a thesis
  not well maintained, mostly non-compatible with other code
Targeting specific problems
Open Source
General
solution
Custom code integration
Design once,
model often
Rust: fast,
memory safe
Our Approach: OPOSSUM OPen-source Optics Simulation System and Unified Modeler
Open Source, accessible for all
Decouple system design from modeling: setup design once, model/analyze in numerous ways
Platform for custom-code integration
Extensible to specific needs
Holistic simulation of large-scale laser facilities
Modern backend, written in Rust for high maintainability, memory safety
Introduction

## Slide 3: Outline
Nodes
Analyzer
Report
Code examples
Code-Statistics
Near-future plans

## Slide 4: Node Geometry / Positioning
„Conventional“ Approach (ZEMAX, Code V, OSLO,…)
  Using absolute coordinates
  Using coordinate breaks
Our Approach
  Use relative positioning through calculation of an optical axis
  Most optical systems easy to model
  Absolute positioning still possible
  Needs testing for inconsistencies
non flexible (but sometimes necessary…)
causes headache …!!!
How to define a node position in 3D space?

## Slide 5: Node Geometry / Positioning II
Position first node (typ. source) absolutely in 3D space.
Define relative distance to next node along the current optical axis.
Define local orientation of node (tilt, decenter of anchor point)
Define relative distance to next node along the current optical axis.

## Slide 6: Node Geometry / Positioning II
Examples
Minor drawback: inconsistencies may occur (but can be checked for):
mirrors in double-pass
flat -> curved mirror

## Slide 7: Nodes – Node types
Special nodes:
Source:
  Holds the initially defined light
  Energy distribution: Uniform, General 2D Gaussian
  Position distribution: Hexapolar, Hexagonal, Fibonacci, Random, Sobol, Grid
  Shape: Ellipse, Rectangle
  Spectrum: Gaussian
Hexapolar
General 2D Gaussian
Rectangle
Spectrum

## Slide 8: Nodes – Node types
Special nodes:
Source:
  Holds the initially defined light
  Energy distribution: Uniform, General 2D Gaussian
  Position distribution: Hexapolar, Hexagonal, Fibonacci, Random, Sobol, Grid
  Shape: Ellipse, Rectangle
  Spectrum: Gaussian
Nodegroup
  Allows grouping of nodes, e.g., multiple lenses as a telescope
  Infinite nesting (groups in groups) possible
Example: HHTS

## Slide 9: Nodes – Node types
Special nodes:
Source:
  Holds the initially defined light
  Energy distribution: Uniform, General 2D Gaussian
  Position distribution: Hexapolar, Hexagonal, Fibonacci, Random, Sobol, Grid
  Shape: Ellipse, Rectangle
  Spectrum: Gaussian
Nodegroup
  Allows grouping of nodes, e.g., multiple lenses as a telescope
  Infinite nesting (groups in groups) possible
Detector nodes:
Energy
Fluence
Spectrum
Spot diagram
Wavefront
Wavefront
FF Fluence
FF Spot diagram

## Slide 10: Nodes – Node types
Special nodes:
Source:
  Holds the initially defined light
  Energy distribution: Uniform, General 2D Gaussian
  Position distribution: Hexapolar, Hexagonal, Fibonacci, Random, Sobol, Grid
  Shape: Ellipse, Rectangle
  Spectrum: Gaussian
Nodegroup
  Allows grouping of nodes, e.g., multiple lenses as a telescope
  Infinite nesting (groups in groups) possible
Detector nodes:
Energy
Fluence
Spectrum
Spot diagram
Wavefront
Generic nodes:
Spherical lens
Cylindrical lens
Paraxial Lens
Wedge
Thin mirror (single surface)
Ideal filter
Reflective grating
Ideal beam splitter

## Slide 11: Nodes – surfaces & Refraction
Every node holds one or multiple optical surfaces
An optical surface consists of:
  A geometrical surface: E.g., a plane, a sphere, cylinder…
  An aperture
  A coating: Ideal-Ar, constant reflectivity or Fresnel
  LIDT information (as input parameter, not yet calculated)
The refractive index of a node can be described by:
  A constant value
  Sellmeier equations
  Schott formula
  Conrady formula

## Slide 12: Analyzer
Simple energy analyzer
  Energy flow and splitting between nodes
  rudimentary but very fast
Sequential Ray-tracing analyzer:
  Rays propagate from node to node guided along a topologically sorted flow-graph
  Implementation of detectors allow to evaluate parameters such as fluence, energy, wavefront etc
Semi-sequential ghost-focus / lidt analyzer
  Rays propagate similar to ray-tracing analyzer but can bounce off of surfaces
  Propagation is handled iteratively in forward and backward direction
  Fluence on optical surfaces is evaluated and a report is generated if the fluence exceeds the LIDT
Node 1
Node 2
Node 3
E1
E2
E3
Node 1
Node 2
Node 3
Rays1
Rays2
Rays3
Node 1
Node 2
Node 3
Node 1
Node 2
Node 3
Iteration 1: forward
Iteration 2: backward
Iteration 3: forward…

## Slide 13: Reports
Reports are generated as HTML to be viewed in a web browser
Reported data is sorted by its position in groups and nodes
Specialized analyzers, such as the ghost focus analyzer, create the reports depending only on their analysis purpose, but not on the detectors in the system
Example: FF spot diagram in the 1w arm of the HHTS

## Slide 14: Reports
Example Ghost Focus analyzer
Telescope with two bi-convex lenses
Wedge after telescope
Every damaging ray bundle can be traced back to its origin, including the bounces

## Slide 15: Code examples
Only few lines of code to define a treacy compressor
Flowgraph representation of treacy compressor
Ray tracing output of Beam with Gaussian spectrum (8nm fwhm at 1054 nm)

## Slide 16: Code Statistics
31600 lines of code
4500 lines of comments
1098 commits, average of 2 commits per day
255 tickets closed
> 630 unit tests

## Slide 17: Near-Future plans
GUI implementation for drag & drop optical-system design
Polarization handling
Real beam splitters
Amplifier via Frantz-Nodvik implementation
Additional nodes: parabolas, polarizers, etc.
Full code coverage with unit tests